## Slide 1: A NEW DIGITAL IMAGE COMPRESSION ALGORITHM BASED ON NONLINEAR DYNAMICAL SYSTEMS
R I T
Rochester Institute of Technology
Dr. Chance M. Glenn1,2, Sr., Prof. Michael Eastman2, Gaurav Paliwal
(1) Director – Laboratory for Advanced Communications Technology (LACT)
The Center for Advancing the Study of Cyber Infrastructure (CASCI)
(1), (2) Professor – ECTET Department, College of Applied Science & Technology
Rochester Institute of Technology
Rochester, New York (USA)

## Slide 2
R I T
Rochester Institute of Technology
Overview
This talk describes the basis for and implementation of a new digital signal compression algorithm that has its foundation in nonlinear dynamics.
This work represents a collaborative effort between the RIT, the LACT, and Syncrodyne Systems Corporation.
We are exploring the limits of the potential of chaotic dynamics as a root for this concept. We are reporting on our results to date. We believe significant improvement is possible.
We will show potential for digital streaming and digital rights management applications.

## Slide 3
R I T
Rochester Institute of Technology
Overview
DYNAMAC (dy-NAM-ac) stands for dynamics-based algorithmic compression. The basic foundation of the process lies in the realizations that (a) chaotic oscillators are dynamical systems that can be governed by mathematical expressions, and (b) chaotic oscillators are capable of producing diverse waveform shapes.
Further, if we improve the chaotic oscillator’s ability to produce diverse waveform shapes, we increase the probability of matching arbitrary digital sequence segments.

## Slide 4
R I T
Rochester Institute of Technology
Chaotic Dynamics
where
Ve
Vc
R
Re
L
Ce
C
+
Vee
Q
+
Vcc
Circuit diagram:
A typical chaotic oscillator is the Colpitts system.
The Colpitts circuit is a typical circuit topology used in the engineering design of oscillators.
Equations of motion:

## Slide 5
Rochester Institute of Technology
Chaotic Dynamics
State-space plot:

## Slide 6
Rochester Institute of Technology
Chaotic Dynamics
Time-dependent waveforms
Note the waveform variation in these segments
Initial conditions
We’ve expanded upon this method

## Slide 7
Rochester Institute of Technology
Chaotic Dynamics
Important feature:
Time diversity (positive Lyapunov exponent, positive entropy)
A set of initial conditions are spread by the dynamics of the system
s = s0edt
dt = 10 s
in the direction of iL,
= 4.5 x 105
(+) expansion
(-) compression
s0

## Slide 8
Rochester Institute of Technology
The DYNAMAC Algorithm

## Slide 9
Rochester Institute of Technology
The DYNAMAC Algorithm
Digital Sequence
Initialization file
Sequence
Parser
C
Combined Chaotic Oscillation Matrix
(32x65536x16)
CO Decimator
Scaling
Comparator
Input Buffer
x[n]
xp[n]
Ns
Ns
cn[n]
[n]
c[n]
Nc
f
D-bite
generator
Nt
Ni
Nc
Fixed Storage
Ns
Ns
Ni
Nt
Nc
Ns
D = [D1,D2,D3]
BLOCK DIAGRAM
(EXAMPLE)

## Slide 10
Rochester Institute of Technology
The DYNAMAC Algorithm
Symbolically, we can describe a DYNAMAC operator as
, where
is the original digital sequence,
is the combined chaotic oscillation matrix (static), and
is the matrix ordering sequence.
where
then compression occurs. We reproduce the digital sequence by
The point-wise error between the original and reconstructed sequence is
is the total error between the sequences. E = 0 mean lossless compression.
if
is the length function

## Slide 11
Rochester Institute of Technology
The DYNAMAC Algorithm
Image Error Measures:
Mean-square error
Peak signal-to-noise ratio

## Slide 12
Rochester Institute of Technology
Selected Results
Compression Ratio | 3.6:1 | 7.1:1 | 14.2:1
MSE | 17.74 | 41.62 | 112.62
PSNR | 35.70 dB | 32.02 dB | 27.75 dB
ORIGINAL

## Slide 13
Rochester Institute of Technology
Selected Results
Compression Ratio | 3.6:1 | 7.1:1 | 14.2:1
MSE | 115.35 | 277.59 | 658.54
PSNR | 27.52 dB | 23.70 dB | 19.96 dB
ORIGINAL

## Slide 14
Rochester Institute of Technology
Other Implications
CCO Matrix
1 2 3, …, 65536
1
2
3
.
.
.
32
Orderings:
k1 = [1,2,3,…, 32]
There are 32! Different non-repeating orderings possible.
If the ordering is changed, the image can be scrambled.
k can act as a key.
Digital Rights Management

## Slide 15
Rochester Institute of Technology
Other Implications
Decompressed image with k1 ordering
Decompressed image with alternate ordering
(scrambled)

## Slide 16
Rochester Institute of Technology
Other Implications
Digital Streaming
1
2
3
N
1
…
1
2
3
N
…
1
2
3
4
5
D-bites are independent of each other
Image can be reconstructed in sequential order without knowledge of past or future
DECOMPRESSION
N

## Slide 17
Rochester Institute of Technology
Conclusions
The DYNAMAC algorithm is viable for compression of digital images
Other digital data types (audio, video, etc.) are capable of being compressed by the algorithm
We are developing hardware for rapid implementation of the compression engine.
There are implications for digital rights management, digital streaming, and digital redundancy.
We are presently making strides in the improvement of compression ratio, image quality, and processing time.
We are developing relationships with industry partners for potential commercialization.

## Slide 18
Rochester Institute of Technology
References
http://www.ph.tn.tudelft.nl/Courses/FIP/frames/fip.html, “Image Processing Fundamentals”.
Gleick, J., CHAOS: Making a New Science, Penquin Books, New York, NY, 1987.
Glenn, C. M., “High-Gain, High-Efficiency Power Amplification for PCS”, International Symposium on Advanced Radio Technology Symposium Digest, March 2003.
Glenn, C. M., “Weak Signal Detection by Small-Perturbation Control of Chaotic Orbits”, 1996 IEEE-MTT Symposium Digest (Invited Paper), March 1996.
Moon, F, Chaotic Vibrations, Wiley & Sons, New York, 1987.
Hasler, M. J., Electrical Circuits with Chaotic Behavior, Proceeding sof the IEEE, vol. 75, no. 8, August 1987.
Blahut, R. E., Principles and Practice of Information Theory, Addison-Wesley Publishing Company, New York, 1987.
http://www.debugmode.com/imagecmp/,“An Introduction to Image Compression”.
Anderson, P.G., "Linear Pixel Shuffling for Image Processing, an Introduction", The Journal of Electronic Imaging. April 1993, pp. 147-154.
Ott, E.,Gregobi, C., Yorke, J.A., Physical Review Letters 64, 1196 (1990).
Ott, E., Chaos in Dynamical Systems, Cambridge Univ. Press, Canada, 1993.

## Slide 19
Rochester Institute of Technology
Thanks
IADAT (city of Madrid)– acceptance of paper and hospitality
Colleagues – Prof. Michael Eastman (Chair ECTET Dept. RIT) and Gaurav Paliwal (graduate student)
CASCI (Professor Guy Johnson, Director) – laboratory support
Syncrodyne Systems Corporation – technology support